## Slide 1
Smart Aquarium Fish Health
Monitoring System
Real-time AI-powered fish health detection with IoT aquarium automation
Team Members
Nawneet Kumar | Sanket Vaidya
Mentor
Dr. Rishikant Rajdeepak
April 14, 2026 | Final Year Project Presentation
92.5%
Detection Accuracy
95.3%
Precision
Real-time
30 FPS (GPU)
7 Sensors
IoT Integration

## Slide 2
PROBLEM STATEMENT
Why do aquarium fish die silently?
Late Detection
Fish disease symptoms are subtle. By the time owners notice color changes or lethargy, the disease has often progressed beyond treatment.
Manual Monitoring
Aquarium owners must manually check water parameters, observe fish behavior, and maintain feeding schedules. Human oversight is inconsistent and error-prone.
No Early Warning
Behavioral changes (swimming patterns, isolation, surface gasping) precede visible symptoms by 4-5 days, but humans cannot track individual fish behavior 24/7.
OUR SOLUTION
YOLOv8 CNN trained on fish tank footage for real-time detection (92.5% mAP50)
Per-fish adaptive baselines using Welford's algorithm — each fish compared to its OWN normal
Z-score anomaly detection across 9 health indicators (behavioral + visual)
ESP32-based IoT system with 7 sensors for automated water quality monitoring
Automated feeding, heating, lighting, and aeration based on sensor data and schedules
Live web dashboard with health scores, alerts, and tuning controls

## Slide 3
METHODOLOGY
AI Pipeline — Detection to Alert
1
Detection
YOLOv8n CNN
Custom-trained on fish tank footage. 92.5% mAP50, 95.3% precision.
2
Tracking
Enhanced SORT
Kalman filter + appearance Re-ID. Hungarian algorithm for optimal matching.
3
Health Analysis
Visual + Behavioral
5 visual features (color, texture, shape) + 7 behavior metrics (speed, pattern).
4
Adaptive Baseline
Welford's Algorithm
Per-fish running mean/std. O(1) memory. Ready after 150 samples (~25 sec).
5
Anomaly Detection
Z-Score + Consensus
9-metric weighted consensus. Z > 2.0 = concern. 73% behavioral, 27% visual.
6
Alert Generation
4-Stage Filter
Baseline wait + track maturity + sustained check + 60s cooldown.
KEY ALGORITHMS & TECHNIQUES
Welford's Online Algorithm
Numerically stable single-pass variance. O(1) memory per fish per metric.
Z-Score Anomaly Detection
Compares each fish to its OWN baseline. Z = |current - mean| / std.
EMA Smoothing (alpha=0.15)
Exponential moving average removes noise. Responds in ~7 seconds.
Hysteresis State Machine
Dead-band gaps prevent status flickering. 4 states: Healthy/Concern/Warning/Critical.

## Slide 4
METHODOLOGY
IoT Hardware — ESP32 Aquarium Automation
SENSORS (INPUT)
DS18B20
Temperature
Water temp in Celsius
GPIO 4
PH4502C
pH Sensor
Acidity/alkalinity (0-14)
GPIO 34
SEN0189
Turbidity
Water clarity (NTU)
GPIO 35
TDS V1.0
TDS Meter
Dissolved solids (ppm)
GPIO 33
DS3231
RTC Clock
Time & date keeping
I2C
TTP223
Touch Sensors
User input (LED control)
GPIO 23, 5
Pot.
Potentiometer
LED brightness control
GPIO 32
ACTUATORS (OUTPUT)
Relay x2
Light + Heater
Time/temp controlled
GPIO 26, 27
SG90 Servo
Fish Feeder
Scheduled + manual feed
GPIO 16
Air Pump
Oxygenation
Time-based aeration
GPIO 2
PC Fan
Cooling
Button-triggered airflow
GPIO 19
WS2812B
LED Strip
RGB effects, touch control
GPIO 18
1W LEDs
Status LEDs
Red=feeding, Blue=servo
GPIO 17, 25
DISPLAYS
SSD1306 (0x3C)
pH, Turbidity, TDS, Water condition
SSD1306 (0x3D)
Time, Date, Temperature, Heater status
MAX7219
Animated clock, Scrolling date
ESP32 WROOM — Central Controller
Reads all sensor data -> Processes logic & schedules -> Controls all actuators & displays TIP144/TIP142 transistors switch high-current loads (pump, fan, LEDs)

## Slide 5
RESULTS & ANALYSIS
Model Performance & System Evaluation
92.5%
mAP50
Detection accuracy across all test frames
95.3%
Precision
Very few false detections
84.8%
Recall
Catches 84.8% of all fish in frame
76.1%
mAP50-95
Strict multi-threshold accuracy
30 FPS
GPU Speed
Real-time inference on CUDA devices
~6 MB
Model Size
YOLOv8n nano model lightweight deploy
ADAPTIVE HEALTH SCORING
Per-fish baselines converge in ~25 seconds (150 samples)
Healthy fish score 70-85% (vs 45-70% with fixed thresholds)
Z-score detection catches behavioral changes 4-5 days before visible symptoms
Multi-indicator consensus: 2+ anomalous metrics needed to trigger concern
Hysteresis state machine eliminates status flickering completely
Alert latency: 5-10 seconds for genuine health concerns
IoT SYSTEM PERFORMANCE
All 7 sensors reading accurately in real-time
Automated feeding on schedule via servo motor
Temperature-controlled heater activation
Time-based lighting and aeration cycles
Dual OLED + MAX7219 displays showing live data
Touch-controlled RGB LED lighting effects
Custom model vs Generic YOLO:
92.5% mAP50 (custom) vs 30-50% mAP50 (generic) — No false positives on hands, faces, or decorations

## Slide 6
CONCLUSION
Summary & Future Work
What We Built
End-to-end fish health monitoring: camera to alert in real-time
CNN-based detection (92.5% mAP50) + adaptive per-fish baselines
Statistical anomaly detection outperforms fixed thresholds significantly
Full IoT automation: feeding, heating, lighting, aeration, water monitoring
Live web dashboard with health scores, alerts, and parameter tuning
Behavioral analysis detects illness days before visible symptoms appear
Project Status
Work Completed:
85%
Expected Completion:
May 2026
Remaining Work
Hardware-software integration (ESP32 + dashboard link)
Extended testing with multiple fish species
Mobile app notifications for alerts
REFERENCES
Ultralytics YOLOv8 (2023) — Real-time object detection architecture
Bewley et al. (2016) — SORT: Simple Online and Realtime Tracking
Welford, B.P. (1962) — Numerically stable single-pass variance computation
Kalman, R.E. (1960) — Optimal state estimation for linear dynamic systems
Kuhn, H.W. (1955) — The Hungarian Algorithm for assignment problems
OpenCV Library — Computer vision and image processing
Espressif ESP32 — IoT microcontroller platform documentation
Thank You | Questions?